## Slide 1: Chapter 1 The PIC18 Microcontroller

## Slide 2: Objective
  Von Neumann and Harvard Architectures
  Compare the contrasts in microprocessors and microcontrollers.
  Explain the concept of embedded system.

## Slide 3: Section 1.1 Von Neumann and Harvard Architectures

## Slide 4: Harvard vs von Neumann Architecture
von Neumann – uses the same address and data bus for code ROM space and data RAM space.
Harvard – uses different address and data buses to access code ROM space and data RAM space.
von Neumann architecture is slow because ROM and RAM cannot be accessed simultaneously.
Implementing Harvard architecture is expensive.
von Neumann Harvard
Notes: esp when the RAM and ROM space are external to the CPU.
e.g., Pentium μP with 64-bit data bus and 32-bit address bus needs about 100 wires. Number of wires is doubled for Harvard architecture.

## Slide 5: Von Neumann Architecture is Slow
 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30
 |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  | 
1
2
3
4

## Slide 6: Advantage of Harvard Architecture (easy for pipeline implementation)
 | 30 | 30 | 30 | 30 | 30
 |  |  |  |  | 
 |  |  |  |  | 
 |  |  |  |  | 
 |  |  |  |  | 
1
2
3
4

## Slide 7: Disadvantage of Harvard Architecture
μP 64-bit data bus and 32-bit address bus needs about 200 wires.
Notes: More bus lines are needed
More cost

## Slide 8: Section 1.2 microprocessors and microcontrollers

## Slide 9: General-purpose microprocessor
9
CPU
General-Purpose Micro-processor
RAM
ROM
I/O Port
Timer
Serial COM Port
Data Bus
Address Bus
Figure 1-1 (a) General-Purpose Microprocessor System
CPU for Computers
No RAM, ROM, I/O on CPU chip itself
Example：Intel’s x86, Motorola’s 680x0
Many chips on mother’s board
Notes: 2019/1/29

## Slide 10: Microcontrollers
Embedded Systems
  Operations managed behind the scenes by a microcontroller
Microcontroller (MCU)
  An integrated electronic computing device that includes three major components on a single chip
    Microprocessor (MPU)
    Memory
    I/O (Input/Output) ports
10
Notes: 10

## Slide 11: Microcontrollers
Support Devices (peripheral)
a device attached to a computer
  Timers (counting number of pulses)
  A/D converter (Analog to Digital )
  Serial I/O (example keyboard to main board)
All components connected by common communication lines called the system bus.
11
Notes: 11

## Slide 12: Microcontroller
12
RAM
ROM
I/O Port
Timer
Serial COM Port
Figure 1-1 (b) Microcontroller
CPU
A smaller computer
On-chip RAM, ROM, I/O ports...
Example：Motorola’s 6811, Intel’s 8051, Zilog’s Z8 and PIC 18
A single chip
Notes: 2019/1/29
12

## Slide 13: Microprocessor v.s. Microcontroller
13
Microprocessor
CPU is stand-alone, RAM, ROM, I/O, timer are separate
Designer can decide on the amount of ROM, RAM and I/O ports.
General-purpose
Expensive
Microcontroller
CPU, RAM, ROM, I/O and timer are all on a single chip
Fix amount of on-chip ROM, RAM, I/O ports
Single-purpose
Cheap
For applications in which cost, power and space are critical
Notes: 2019/1/29

## Slide 14: Section 1.3 Embedded System

## Slide 15: Embedded System
15
Embedded system means the processor is embedded into that application.
An embedded product uses a microprocessor or microcontroller to do specified tasks only.
In an embedded system, there is only one application software that is typically burned into ROM.
Some embedded products using microcontrollers. Example：printer, keyboard, video game player, door opener, copier, ABS,
fax machine, camera, cellular phone,
keyless entry, microwave...
Notes: 2019/1/29
Eg: mouse

## Slide 16: Embedded System
16
Notes: 2019/1/29

## Slide 17: Processors in Embedded Systems
Which is your choice for an embedded product？
microcontroller
  cost down
  embedded processor ＝ microcontroller
  In future, an entire computer on a chip
  high-end embedded systems may use microprocessors

## Slide 18: Three criteria in Choosing a Microcontroller
meeting the computing needs of the task efficiently and cost effectively
  speed, the amount of ROM and RAM, the number of I/O ports and timers, size, packaging, power consumption
  easy to upgrade
  cost per unit
availability of software development tools
  assemblers, debuggers, C compilers, emulator, simulator, technical support
wide availability and reliable sources of the microcontrollers.

## Slide 19: Basic Data Format (8-bit)
Unsigned Integers: All eight bits (Bit7 to Bit0) represent the magnitude of a number
  Range 00 to FF in Hex and 0 to 255 in decimal
19
330_01
Notes: 19

## Slide 20: Basic Data Format (8-bit)
Signed Integers: Seven bits (Bit6 to Bit0) represent the magnitude of a number.
  The eighth bit (Bit7) represents the sign of a number. The number is positive when Bit7 is zero and negative when Bit7 is one.
  Positive numbers: 00 to 7F (0 to 127)
  Negative numbers: 80 to FF (-1 to -128)
  All negative numbers are represented in 2’s complement
20
330_01
Notes: 20

## Slide 21: Basic Data Format (8-bit)
Binary Coded Decimal Numbers (BCD)
  8 bits of a number divided into groups of four, and each group represents a decimal digit from 0 to 9
  Four-bit combinations from A through F in Hex are invalid in BCD numbers
    Example: 0010 0101 represents the binary coding of the decimal number 25 which is different in value from 25H.
21
330_01
Notes: 21

## Slide 22: Basic Data Format (8-bit)
American Standard Code for Information Interchange (ASCII)
  Seven-bit alphanumeric code with 128 combinations (00 to 7F)
  Represents English alphabet, decimal digits from 0 to 9, symbols, and commands
22
330_01
Notes: 22

## Slide 23: Section 1.4 Overview of PIC18

## Slide 24: PIC18F Microcontroller Families
PIC microcontrollers are designed using the Harvard Architecture which includes:
  Microprocessor unit (MPU)
  Program memory for instructions
  Data memory for data
  I/O ports
  Support devices such as timers

## Slide 25: Microprocessor Unit
Includes Arithmetic Logic Unit (ALU), Registers, and Control Unit
  Arithmetic Logic Unit (ALU)
    Instruction decoder
      16-bit instructions
    Status register that stores flags
      5-bits (refresh data)
    WREG – working register
      8-bit accumulator

## Slide 26: Microprocessor Unit
  Registers
    Program Counter (PC)
      21-bit register that holds the program memory address while executing programs
    Bank Select Register (BSR) (PIC18F only)
      4-bit register used in direct addressing the data memory
    File Select Registers (FSRs)
      12-bit registers used as memory pointers in indirect addressing data memory
  Control unit
    Provides timing and control signals to various Read and Write operations

## Slide 27: PIC18F - Address Buses
Address bus
  21-bit address bus for program memory addressing capacity: 2 MB of memory
  12-bit address bus for data memory addressing capacity: 4 KB of memory

## Slide 28: Data Bus and Control Signals
Data bus
  16-bit instruction/data bus for program memory
  8-bit data bus for data memory
Control signals
  Read and Write

## Slide 29: PIC18F452/4520 Memory
Program Memory: 32 K
  Address range: 000000 to 007FFFH
Data Memory: 4 K
  Address range: 000 to FFFH
Data EEPROM
  Not part of the data memory space
  Addressed through special function registers

## Slide 30: PIC18F452/4520 Memory
Program memory
Data memory

## Slide 31: PIC18F452/4520 – Data Memory with Access Banks

## Slide 32: PIC18F452 I/O Ports
Five I/O ports
  Digital IO is the most fundamental mode of connecting a MCU to external world. The interface is done using what is called a PORT.
  The IO ports can be programmed as input or output.
  PORT A through PORT E
  Most I/O pins are multiplexed
  Generally have eight I/O pins with a few exceptions
  Addresses already assigned to these ports in the design stage
  Each port is identified by its assigned SFR

## Slide 33: PIC18F452—I/O Ports A and B

## Slide 34: MCU Support Devices
Timers
  Capture, Compare and PWM (CCP Modules)
Serial Communications
  Master Synchronous Serial Port (MSSP)
  Addressable USART
A/D converter
Parallel Slave Port (PSP)
Data EEPROM

## Slide 35: MCU Support Devices

## Slide 36: PIC18F Special Features
Sleep mode
Watchdog timer (WDT)
Code protection
In-circuit serial programming
In-circuit debugger
Notes: WDT : provide program from reset
PIC18F will auto reset itself, thus WDT is needed

## Slide 37
PIC18F4X2 Architecture Block Diagram

## Slide 39: PIC18F Instructions and Assembly Language
Has 77 instructions
  Earlier PIC family of microcontrollers have either 33 or 35 instructions
In PIC18F instruction set, all instructions are 16-bit word length except four instructions that are 32-bit length

## Slide 40: Instruction Description and Illustrations
Copy (Move) 8-bit number (Literal) into W register
  Mnemonics: MOVLW 8-bit
  Binary format:
0000 1110 XXXX XXXX (any 8-bit number)
Copy (Move) contents of W register into PORTC (File)
  Mnemonics: MOVWF PORTC, a
    (‘a’ indicates that PORTC is in the Access Bank)
  Binary format:
0110 1110 1000 0010 (82H is PORTC address)
Notes: Instruction: 2 bytes

## Slide 41: Illustrative Program: Displaying a Byte at an I/O Port
Problem statement:
  Write instructions to light up alternate LEDs at PORTC
Hardware:
  PORTC
    bidirectional (input or output) port; should be setup as output port for display
  Logic 1 will turn on an LED

## Slide 42: Illustration
Interfacing LEDs to PORTC

## Slide 43: Illustration
Program (software)
  Logic 0 to TRISC sets up PORTC as an output port
  Byte 55H turns on alternate LEDs
    MOVLW 00 ;Load W register with 0
    MOVWF TRISC,0 ;Set up PORTC as output
    MOVLW 0x55 ;Byte 55H to turn on LEDS
    MOVWF PORTC,0 ;Turn on LEDs

## Slide 44: PIC18 Simulator IDE

## Slide 45: Embedded System
Microcontroller-based
Time and
Temperature
System

## Slide 46: You are able to
Compare and contrast microprocessors and microcontrollers
Describe the advantages of microcontrollers for some applications
Explain the concept of embedded systems
Discuss criteria to consider in choosing a microcontroller
Explain the variations of speed, packaging, memory, and cost per unit and how these affect choosing a microcontroller
Some basic feature of PIC18